NRF24L01 – Radio network

Application

Control / bridge
Application
Mesh

Data
(No Ack Broadcast)
Network
(dev ↔ dev comms)

Plat. GPIO
Plat. spi
nrf24l01

GPIO
spi

SPI and GPIO classes used by nRF24L01 code are pure virtual classes, with a platform implementation needed to be passed to the constructor. This allows all library to be platform independent with the SPI and GPIO implementations being the only platform specific code required.

The nRF24L01 code provides access to ALL features offered by the device. This is pulled together into a basic communications system by the Data layer.

Recommended default channel 2498 MHz – this avoids WiFi channels in the 2.4 GHz range. (RF_CH = 0x62)

Broadcast Address – receive pipe 0 on ALL radios = 0x01 0x00 0x00 0x00 0x01

The system of radios is configured to use the Enhanced ShockBurst mode with variable length data.

First byte in message = control byte

Control bytes in Data layer
00 – Broadcast data (no ack)
sent to address 0x01 0x00 0x00 0x00 0x01
Free form data within the remaining 31 bytes of payload data – application dependent