Wireless pixel V1 protocol

Proposed protocol for the version 1 pixel – will need to verify this can all be implemented within the limited memory of the ATTiny85.

This protocol uses only the broadcast service of the underlying nrf24l01 library.

There are 2 options to target the commands:
    - All pixels in range
    - Pixels belonging to a specific group
There are 2 options when specifying colours:
    - Standard colours (0-8)
    - RGB values

On the ATTiny85 and other CPUs the EPROM memory is used to store standards colour values and group ID.

Note : RGB Sequences removed due to memory constraints of ATTiny85

# Basic command structure
<Group target> <RGB colours> <remaining 6bits> [ optional additional bytes of command]
- Group target is 0 if all pixels or 1 for a specific group
- RGB colours is 0 if using standard colours or 1 for RGB values

Group targets are identified by an IDs, which are 2 byte -> 0 - 65535.

# Standard colours
Initial values (RGB)
0 (000) - 0, 0, 0
1 (001) - 255, 0, 0
2 (010)- 0, 255, 0
3 (011)- 0, 0, 255
4 (100)- 255, 255, 0
5 (101)- 0, 255, 255
6 (110)- 255, 0, 255
7 (111)- 255, 255, 255

Commands are of format (1-byte + optional additional bytet):
<Group ID><0><CCC><colour/sequence - 3 bits>
where:
Group ID is 1 bit : 0 = all pixel broadcast ; 1 – group ID specified as additional 2 bytes
CCC = 3 bit command code
ccc = 3 bit standard colour code or sequence ID

Commands:
0 (000)	set colour	0b00000ccc / 0b10000ccc <id-hi><id-lo>
1 (001)	fade to colour	0b00001ccc <time> / 0b10000ccc <id-hi><id-lo> <time>	additional byte specifying time in 1/100 seconds
2 (010)	Play sequence	0b00010sss / 0b10010sss <id-hi><id-lo>
3 (011)	Play sequence with fade	0b00011sss <time> / 0b10011sss <id-hi><id-lo> <time>
4 (100)	loop sequence	0b00100sss / 0b10100sss <id-hi><id-lo>
5 (101)	loop sequence with fade	0b00101sss <time> / 0b10101sss <id-hi><id-lo> <time>
6 (110)	update colour	0b00110ccc <R><G><B> / 0b10110ccc <id-hi><id-lo> <R><G><B>
7 (111)	update sequence	0b00111sss <n> [cccttttt]n / 0b10111sss <id-hi><id-lo> <n> [cccttttt]n	n = number of steps in seq. / ccc = colour, ttttt = time (tenth of seconds 0 - 31)

<Group ID><1><00><CCCC>
0 (0000)	Set RGB colour	0b01000000 <R><G><B> / 0b11000000 <id-hi><id-lo> <R><G><B>
1 (0001)	Fade to RGB colour	0b01000001 <R><G><B> <time> / 0b11000001 <id-hi><id-lo><R><G><B> <time>
2 (0010)	Store updates	0b01000010 / 0b11000010	Modifying sequences and standard colours does not write to store, so will revert on reboot. This command forces changes to storage to survive reboot
3 (0011)	Set pixel ID	0b01000011 <new id-hi><new id-lo> / 0b11000011 <id-hi><id-lo> <new id-hi><new id-lo>

<Group ID><1><CCC><SSS> (CCC > 1 so as not to overlap with previous command group)
2 (010)	Play RGB sequence	0b01010SSS / 0b11010SSS <id-hi><id-lo>
3 (011)	Play RGB sequence with fade	0b01011SSS <time> / 0b11011SSS <id-hi><id-lo> <time>
4 (100)	Loop RGB Sequence	0b01100SSS / 0b11100SSS <id-hi><id-lo>
5 (101)	Loop RGB Sequence with fade	0b01101SSS <time> / 0b11101SSS <id-hi><id-lo> <time>
6 (110)	update RGB sequence	0b01110SSS <n> <np> [<R><G><B><time>]n / 0b11110SSS <id-hi><id-lo> <n> [<R><G><B><time>]n	np specifies number of sequence elements in this command, use continuation to add remaining sequence steps
7 (111)	Update sequence continued from position	0b01111SSS <p> <n> [<R><G><B><time>]n / 0b11111SSS <id-hi><id-lo> <p> <n> [<R><G><B><time>]n	Finite sized packet, so use this command to complete sequence if overflow a single packet. Position p specifies where this command should start in sequence. Sequences start at position 0.

Summary of commands
Broadcast					Group
0	Set colour 0		40	Set RGB colour	80	Set colour 0	C0
1	Set colour 1		41	Fade to RGB colour	81	Set colour 1	C1
2	Set colour 2		42	Store updates	82	Set colour 2	C2
3	Set colour 3		43		83	Set colour 3	C3
4	Set colour 4		44		84	Set colour 4	C4
5	Set colour 5		45		85	Set colour 5	C5
6	Set colour 6		46		86	Set colour 6	C6
7	Set colour 7		47		87	Set colour 7	C7
8	Fade to colour 0		48		88	Fade to colour 0	C8
9	Fade to colour 1		49		89	Fade to colour 1	C9
A	Fade to colour 2		4A		8A	Fade to colour 2	CA
B	Fade to colour 3		4B		8B	Fade to colour 3	CB
C	Fade to colour 4		4C		8C	Fade to colour 4	CC
D	Fade to colour 5		4D		8D	Fade to colour 5	CD
E	Fade to colour 6		4E		8E	Fade to colour 6	CE
F	Fade to colour 7		4F		8F	Fade to colour 7	CF
10	Play sequence 0		50	Play RGB Sequence 0	90	Play sequence 0	D0
11	Play sequence 1		51	Play RGB Sequence 1	91	Play sequence 1	D1
12	Play sequence 2		52	Play RGB Sequence 2	92	Play sequence 2	D2
13	Play sequence 3		53	Play RGB Sequence 3	93	Play sequence 3	D3
14	Play sequence 4		54	Play RGB Sequence 4	94	Play sequence 4	D4
15	Play sequence 5		55	Play RGB Sequence 5	95	Play sequence 5	D5
16	Play sequence 6		56	Play RGB Sequence 6	96	Play sequence 6	D6
17	Play sequence 7		57	Play RGB Sequence 7	97	Play sequence 7	D7
18	Play sequence 0 with fade		58	Play RGB Sequence 0 with fade	98	Play sequence 0 with fade	D8
19	Play sequence 1 with fade		59	Play RGB Sequence 1 with fade	99	Play sequence 1 with fade	D9
1A	Play sequence 2 with fade		5A	Play RGB Sequence 2 with fade	9A	Play sequence 2 with fade	DA
1B	Play sequence 3 with fade		5B	Play RGB Sequence 3 with fade	9B	Play sequence 3 with fade	DB
1C	Play sequence 4 with fade		5C	Play RGB Sequence 4 with fade	9C	Play sequence 4 with fade	DC
1D	Play sequence 5 with fade		5D	Play RGB Sequence 5 with fade	9D	Play sequence 5 with fade	DD
1E	Play sequence 6 with fade		5E	Play RGB Sequence 6 with fade	9E	Play sequence 6 with fade	DE
1F	Play sequence 7 with fade		5F	Play RGB Sequence 7 with fade	9F	Play sequence 7 with fade	DF
20	Loop sequence 0		60	Loop RGB sequence 0	A0	Loop sequence 0	E0
21	Loop sequence 1		61	Loop RGB sequence 1	A1	Loop sequence 1	E1
22	Loop sequence 2		62	Loop RGB sequence 2	A2	Loop sequence 2	E2
23	Loop sequence 3		63	Loop RGB sequence 3	A3	Loop sequence 3	E3
24	Loop sequence 4		64	Loop RGB sequence 4	A4	Loop sequence 4	E4
25	Loop sequence 5		65	Loop RGB sequence 5	A5	Loop sequence 5	E5
26	Loop sequence 6		66	Loop RGB sequence 6	A6	Loop sequence 6	E6
27	Loop sequence 7		67	Loop RGB sequence 7	A7	Loop sequence 7	E7
28	Loop sequence 0 with fade		68	Loop RGB sequence 0 with fade	A8	Loop sequence 0 with fade	E8
29	Loop sequence 1 with fade		69	Loop RGB sequence 1 with fade	A9	Loop sequence 1 with fade	E9
2A	Loop sequence 2 with fade		6A	Loop RGB sequence 2 with fade	AA	Loop sequence 2 with fade	EA
2B	Loop sequence 3 with fade		6B	Loop RGB sequence 3 with fade	AB	Loop sequence 3 with fade	EB
2C	Loop sequence 4 with fade		6C	Loop RGB sequence 4 with fade	AC	Loop sequence 4 with fade	EC
2D	Loop sequence 5 with fade		6D	Loop RGB sequence 5 with fade	AD	Loop sequence 5 with fade	ED
2E	Loop sequence 6 with fade		6E	Loop RGB sequence 6 with fade	AE	Loop sequence 6 with fade	EE
2F	Loop sequence 7 with fade		6F	Loop RGB sequence 7 with fade	AF	Loop sequence 7 with fade	EF
30	Update std colour 0		70	Update RGB sequence 0	B0	Update std colour 0	F0
31	Update std colour 1		71	Update RGB sequence 1	B1	Update std colour 1	F1
32	Update std colour 2		72	Update RGB sequence 2	B2	Update std colour 2	F2
33	Update std colour 3		73	Update RGB sequence 3	B3	Update std colour 3	F3
34	Update std colour 4		74	Update RGB sequence 4	B4	Update std colour 4	F4
35	Update std colour 5		75	Update RGB sequence 5	B5	Update std colour 5	F5
36	Update std colour 6		76	Update RGB sequence 6	B6	Update std colour 6	F6
37	Update std colour 7		77	Update RGB sequence 7	B7	Update std colour 7	F7
38	Update sequence 0		78	Update RGB sequence 0 cont	B8	Update sequence 0	F8
39	Update sequence 1		79	Update RGB sequence 1 cont	B9	Update sequence 1	F9
3A	Update sequence 2		7A	Update RGB sequence 2 cont	BA	Update sequence 2	FA
3B	Update sequence 3		7B	Update RGB sequence 3 cont	BB	Update sequence 3	FB
3C	Update sequence 4		7C	Update RGB sequence 4 cont	BC	Update sequence 4	FC
3D	Update sequence 5		7D	Update RGB sequence 5 cont	BD	Update sequence 5	FD
3E	Update sequence 6		7E	Update RGB sequence 6 cont	BE	Update sequence 6	FE
3F	Update sequence 7		7F	Update RGB sequence 7 cont	BF	Update sequence 7	FF